## Slide 1
If you go further away from the target, the switching frequency gets higher because the oscillator does not need to ramp up so much.
Is the maximum possible switching sequence per second.
The ratio between „target“ (metal)
and no target (no metal) is 1:2.
The maximum switching frequency is reached when:
  the „switch on“ signal t1=50µs
  or
  the „switch off“ signal t2=100µs
The distance sensor to target is Sn/2.
The heigth of the teeth should be >=2xSn
Recommendation for dimensions of a toothed wheel
Switching Frequency f
Notes: The values given are all derived from the sensor standard
The switching frequency indicates the max. possible changes/sec from energized to unenergized status